## Slide 1: Capacitive Torque Sensor
Reference Design
Specifications
Measurable Torque – 100 Nm
Weight - 330g
Resolution - 10 bit
Operating Temp - 0-80 C

## Slide 2
User Needs and Requirements
Light Weight
Accuracy and Precision
Structural Rigidity
Ease of Setup
Stability over time and Environmental Condition
Cost
Shareholders
Users ( Engineers)
Business Owners
Maintenance Technicians
Regulatory Bodies

## Slide 3: Conceptual Design
Isometric View
Front View

## Slide 4
Individual Enclosure Designs

## Slide 5
Conceptual Design Evaluation

## Slide 6: Enclosure Design
Side View
Isometric View
Front View

## Slide 7: Individual Block Diagrams

## Slide 8: Final Block Diagram

## Slide 9: Internal Mechanism Concept
Internal Disks

## Slide 10: Material Selection Analysis using Ansys
Setup With Torsion Bar
Stainless Steel
1 Nm - 7.5104e-007 m
50 Nm - 1.6339e-004 m
Aluminum
1 Nm - 7.0396e-006 m
50 Nm - 1.7599e-004 m
Stainless Steel with Aluminum Alloy
1 Nm - 6.2111e-006 m
50 Nm - 1.5528e-004 m

## Slide 11: Dielectric Material Evaluation
 | PTEF (Teflon) | Polyimide (Kapton) | Alumina Ceramic (Al2O3) | FR4 (Glass Epoxy) | Polycarbonate
Dielectric Constant | 7 | 9 | 10 | 8 | 6
Flexural Strength | 4 | 7 | 9 | 10 | 5
Ease of Machining | 8 | 6 | 3 | 7 | 9
Stability | 9 | 8 | 10 | 8 | 7
Cost | 6 | 4 | 3 | 9 | 10
Total | 34 | 34 | 35 | 42 | 37
According to evaluation , best dielectric material for the project appears to be FR4 (Glass Epoxy).
Dielectric Constant – Around 4.5
Can use CNC milling, laser cutting.
Industry standard PCB material, readily machined by PCB fabrication shops.

## Slide 12
PTEF (Teflon)
Polyimide (Kapton)
Alumina Ceramic (Al2O3)
Calculations

## Slide 13: Capacitive Measuring Techniques
AC Bridge Measurement– Determines an unknown capacitance by balancing an AC bridge circuit (e.g., Schering Bridge) using reference components.
Capacitance to Digital Conversion – A capacitance to digital converter directly measures capacitance and converts it into digital signal.
Phase Sensitive Detection (Lock In Amplifier)– Uses an AC signal, and a phase sensitive detector extracts phase shifts due to capacitance variations.
Charge Discharge Time Measurement – Measures the time for a capacitor to charge/discharge through a known resistor.

## Slide 14: Capacitor Measurement Techniques Evaluation
 | CDC | Lock in Amplifier | Charge Discharge Time Measurement | AC Bridge
Precision | 9 | 10 | 6 | 8
Cost | 5 | 3 | 10 | 7
Complexity | 9 | 4 | 8 | 5
Robustness | 9 | 9 | 6 | 7
Total Score | 32 | 26 | 30 | 27
High Accuracy & Resolution – Provides precise digital output with minimal noise.
Direct Digital Output – Eliminates the need for complex analog processing.
High Speed – Can perform rapid capacitance measurements.
Some CDCs Include Environmental Compensation

## Slide 15
CDC Options
Analog Devices – AD7156
Sensor capacitance : 0 pF up to 13 pF
Sensitivity : up to 3 fF
Adaptive environmental compensation
Analog Devices – AD7156
Sensor capacitance : 4pF
Sensitivity : up to 4 fF
Temperature Sensor on Chip
Texas Instruments– FDC1004
Sensor capacitance : ±15pF
Measurement resolution: 0.5fF
Programmable output rates: 100/200/400 S/s
Capacitor Plate Integration Example